## Slide 1: GPU Architecture and Mali GPU

## Slide 2: Module Syllabus
GPU Architectures
  Hardware Evolution
  GPU Architecture Design Principles
  GPU Rendering Approaches
Mali GPU Family
  Mali Architecture and Data Models
Notes: In this module, we will introduce GPU architectures, including a brief GPU history and an illustration of principles and rendering models.
Then, we will study the Arm Mali GPU family, which are energy-efficient GPUs widely used in mobile applications.

## Slide 3: GPU Architectures: Hardware Evolution
GPU hardware evolution closely tied to evolution in usage patterns
  Desire for improved visual effects driven by games
  More realism, more effects, more screen resolution, more frames per second
Hardware architecture based on desirable software application programming interfaces (API) features
  Incremental extensions to logical graphics pipelines
Real-time rendering with new features needs better hardware
  Incremental addition of fixed-function hardware and programmable units

## Slide 4: OpenGL ES Pipelines:1.0/2.0
Entirely fixed function pipeline
Notes: This slide provides a recap of the previous module’s pipeline diagram.
Remember the transform feedback feature is just included from pipeline 3.0
Green blocks are fixed function, although often configurable (on/off/mode select), and blue blocks are the outputs of the render. These are entirely fixed functions.
The Geometry Processing block operates on each vertex and translates it from model-space coordinates into eye-space coordinate.
The Primitive Assembly block takes groups of vertices and converts them into primitives: points, lines, and triangles in the case of OpenGL ES. This stage is also responsible for determining which of the primitives are visible, discarding them from the pipeline if they are. This includes primitives that are outside of the viewing frustum and primitives that are single-sided and facing away from the view-port.
The Rasterizer block takes each primitive and converts it into a group of pixels known as fragments because each pixel is only a fragment of the whole primitive raster.
The Fragment Processing block takes each fragment and calculates its color and depth (distance from camera) and decides whether it should have been drawn or not.
The Fragment Operations block takes each fragment and performs a standard set of operations:
Pixel ownership: Does this program own this pixel? If not, it is discarded and not drawn.
Scissor, stencil, and depth tests: Is this pixel visible based on stencil and what we have drawn already?
Blending for partially transparent pixels and dithering to hide rendering artifacts on low color-depth displays
The Color Value is the value written in to the Color Buffer output display color for this fragment.
The Depth Value (also known as the Z-value) is the value written in to the Depth Buffer – distance from the viewer – which is used to discard pixels that are further away from the viewer than the current pixel.
The Stencil Value is the updated stencil value that is written back into the Stencil Buffer. This is used to allow per-pixel stencil testing.

## Slide 5: GPU Hardware Generation 1
First commercial GPU hardware appears
  3dfx Voodoo (1996)
  Mali-55
Simple fixed function pipeline
  OpenGL, Direct3D, 3dfx Glide API
CPU runs the vertex processing and T&L
  CPU SIMD provides added performance
GPU runs at least texturing and blending
  Originally no more than texturing accelerators
  Later incorporating primitive assembly and rasterization
Mixed solutions 3D only or 2D/3D
Framebuffer
T&L, Primitive Assembly, Clip/Cull
Rasterization
Input Data
Texturing
Z-Buffer, Blend
CPU
GPU
Notes: Note that most components are nonprogrammable because they use Open GL ES 1.0.

## Slide 6: GPU Hardware Generation 2
Vertex processing moved to the GPU
  ATI Radeon 7500 (1998)
  NVIDIA GeForce (1999)
Fixed-function pipeline entirely on GPU
  DirectX and OpenGL equally supported
Serious performance available
  People start thinking about GPGPU
  Limitations of fixed function pipelines
  Limitations of graphics short cuts
Framebuffer
Rasterization
Input Data
Texturing
Z-Buffer, Blend
T&L
Clip & Cull
Assembly
CPU
GPU

## Slide 7: GPU Hardware Generation 3
Programmable functions
  ATI Radeon 9700 (2002)
  NVIDIA GeForce FX (2002)
  Mali-200 & Mali-400
Typed shaders
  Different programming model for each shader
  Different hardware shader core
  Each optimized for specific role
Programmed in assembly-like languages
  OpenGL ARB, DirectX Shader Models
GPGPU becomes feasible, within limits
  Inaccurate floating-point implementations
  Missing/slow integer performance
Framebuffer
Rasterization
Input Data
Z-Buffer, Blend
Clip & Cull
Assembly
CPU
GPU
Vertex Shader
Fragment Shader
Notes: This diagram shows the hardware architecture for OpenGL 2.0. Note the addition of the programmable vertex shader and fragment shader.

## Slide 8: GPU Hardware Generation 4
Unification of shader hardware
  ATI Radeon X1800 (2006)
  NVIDIA GeForce 8800 (2006)
  Mali Midgard family
Vertex and fragment shader improvement
  Able to run on the same hardware
  Support for longer programs and branching
  Programming done in C-like languages
Still reliant on hardware assist
  Rasterizers, texture samplers, tessellation
Design influenced by GPGPU workloads
  Full IEEE-754 floating point
  Language support CUDA, OpenCL
Framebuffer
Rasterization
Input Data
Z-Buffer, Blend
Clip & Cull
Assembly
CPU
GPU
Vertex Shader
Fragment Shader

## Slide 9: GPU Hardware Generation 5
Color Value
Color Value
Additional pipeline stages, but fundamentally running on the same hardware
  Some minor hardware additions such as tessellator units, but no major architectural shift
Color Value
Depth Value
Stencil Value
Compute Processing
Vertex Processing
Primitive Assembly A
Tessellation Control
Fragment Processing
Fragment Operations
Rasterizer
Geometry Processing
Tessellation Evaluation
Primitive Assembly B
Tessellator
Notes: As a result of hardware improvements, OpenGL ES now accommodates more points of control, specifically tessellation control, geometry processing, and fragment processing.

## Slide 10: Why Go Unified?
Mali-200 and Mali-400 have different shader cores for vertex shading and fragment shading:
  Midgard uses a unified shader core. Why the change?
The main reason is that increased precision requirements for fragment shaders forced the issue:
  When geometry needed fp32 maths and fragment only needed fp16 maths, separate hardware made sense.
  New APIs forced fragment shaders toward fp32, so the need for a separate high-precision core vanished.
Unified cores provide a best-case utilization. Any core can handle any workload, so are kept busy all the time.
Vertex
Fragment
Fragment
Vertex
Idle
Idle
Unified
Vertex
Fragment
Unified
Vertex
Fragment
Fragment

## Slide 11: Tessellation Shaders?
Tessellation allows high detail models to be used with lower cost:
  CPU can work with simpler meshes for animation, physics, etc.
  Lower transfer costs over PCIe for card-based GPUs
Programmatic subdivision of meshes into higher (or merging into lower) triangle density meshes
  Control shader determines how much subdivision to apply to the current triangle patch.
  Tessellator (fixed function) creates the new vertices and primitives based on selected level of detail.
  Evaluation shader moves the new vertices into position and computes per vertex attributes.
Commonly used for programmatic terrain generation and improving character meshes. Developers are not recommended to do tessellation
Tessellation Control
Tessellation Evaluation
Tessellator

## Slide 12: Geometry Processor
Vertex shaders translate programmer-specified vertices
  One vertex in, one vertex out
  No ability to produce new vertices or destroy vertices
Geometry shaders destroy or emit geometry
  Consume vertices and primitives
  Output zero or more vertices/primitives
  Essentially can add or remove geometry on the fly
Procedural dynamic content creation
  Particle systems
  Shadow volume calculation
  Material configuration
Reduce memory bandwidth from CPU to GPU

## Slide 13: GPU Architecture Design Principles: Overview
CPU design is about making a single thread run as fast as possible:
  Pipeline stalls and memory access latency are expensive.
  Increased logic complexity to reduce probability/cost of stalls
  Use of large cache memories to avoid memory misses
GPU design is about maximizing computation throughput:
  Individual thread latency not considered important
  Highly parallelizable problem solving
    Single Instruction Multiple Data
    Single Program Multiple Data
Stream processing
  Read-only inputs and write-only outputs
  Each stream task is computationally independent.

## Slide 14: GPU Design Principles
Design optimized for overall throughput
Power-efficient system
  A number of relatively simple programmable cores
  Supporting fixed-function hardware for some graphic tasks
Instruction stream sharing increases efficiency due to the Single Program Multiple Data model
Use computation to hide memory and pipeline latency
Use wide and fast bandwidth-optimized memory systems
  Modern desktop CPU consumes ~25GB/s
  Modern desktop GPU consumed ~200GB/s
Scalability provided by adding more instances of processing units

## Slide 15: CPU-style Processing Core
Fetch/Decode
ALU
Execution Context
Out-of-Order Execution Control Logic
Accurate Branch Predictor
Memory Prefetch
Large Data Cache
Notes: Now you *could* execute shaders on CPU-style cores to help execute one thread fast, but maybe it would be better to use all that out-of-order, branch prediction, cache, etc. area for something else...

## Slide 16: Remove Excess Logic
Step one
  Remove any logic that is only there to accelerate a single thread.
Result
  Simpler hardware design
  Smaller hardware design
  More power-efficient hardware
Downside
  Branch stalls
  Memory misses
  High memory bandwidth if scaled up by adding more units
1 thread running
Fetch/Decode
ALU
Execution Context

## Slide 17: Lengthen the Pipe
Step two
  Introduce a long barrel pipeline
  Serial execution of 128 different threads
  One thread can complete per cycle
Result
  Can hide memory access latency
  Maximizes utilization of ALUs
  By design issue-related shader programs
    Shared instruction fetch
    Adjacent texture data cached
    Reduced memory bandwidth
Downside
  Branch stalls
128 threads running [only 8 shown]
Fetch/Decode
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Shared Context
Ctx
Ctx
Ctx
Ctx
Ctx
Ctx
Ctx
Ctx

## Slide 18: Scale via Multiple Instances
Eight core design gives
  1024 concurrent active threads
  Up to 8 fragments completed per cycle
Shared L2 cache reduces bandwidth
  Shared data fetch due to spatial locality
Shared L2 Cache

## Slide 19: Summary
Workload
  SPMD – same program runs on multiple independent fragments
  SIMD – each program heavily utilizes vector operations
  Capable of using many ALUs on many cores
Efficiency targets
  Supports massive instruction interleaving for latency hiding
  Is amenable to instruction stream sharing for shared instruction fetch
Think of a GPU as a multi-core processor optimized for maximum throughput.
Notes: Any GPU workload, not just graphics workload (as described earlier)

## Slide 20: GPU Memory Systems
High-end GPU workload
  14x compute performance of high-end CPU
  8x memory bandwidth to feed it
No traditional homogenous cache hierarchy
  GPU memory system is designed for throughput
  Dedicated function-oriented caches can help make use of data locality
Need wide bus, capable of sustaining bandwidth
  Can tolerate a moderate amount of latency
Specialized memory interfaces
  Repack/reorder/interleave memory requests to maximize use of memory bus
  Driver software has control over some data resources, so can repack those to maximize cache efficiency.
Notes: Bandwidth even more critical for GPUs than for CPUs because of the huge number of cores to feed with little caching.
Thanks to latency tolerance, we can buffer memory requests and re-arrange them to make the best of DRAM architecture. CPUs can also do things like this.

## Slide 21: GPU Rendering Approaches
There are a number of approaches to tackling the rendering problem:
  Immediate mode renderer
  Deferred mode renderer
  Hybrid mode renderer
Each design philosophy has a number of dominant characteristics:
  How to package work for processing
  How the processing of that work interacts with the memory system
Each design can get the job done, but not necessarily with the same
  power, performance, memory bandwidth, scalability
Many advantages are measurable, others are philosophical:
  View it as the graphics equivalent of the CISC or RISC argument.

## Slide 22: Competing Architectures: Immediate
Pros
  Simple architecture
  Linear scaling performance with scene complexity
Cons
  High bandwidth usage due to read-modify-write behavior
  Extra memory footprint for depth buffer
  Using alpha channel for blending creates further read-modify-write transactions
  Anti-aliasing requires additional storage and bandwidth
  Performance scales poorly with higher resolutions
for each frame {
for each polygon {
render pixels
}
}
Geometry
Fragment
Renderer
Memory
Write Buffer
Read Texture
Read Buffer
Primitives
FIFO
Color Buffer
Depth Buffer
Scene Data
Stencil Buffer
Notes: While immediate mode rendering has some advantages, there are a significant limitations:
Read-modify-write behavior is required, since all pixels are rendered, then their depth information is read in. Depending on this depth value, the pixels that have been completely overlapped are discarded, assuming all pixels in question are opaque. After this step, the new value of the pixels is written back to the framebuffer. This is a high bandwidth activity.
A memory-hungry depth buffer is required to process each fragment and determine if that fragment sits in front of, or behind, the pixel already in the framebuffer.

## Slide 23: Competing Architectures: Deferred
Pros
  Less redundant processing
  Tile-based, so low memory bandwidth
  Being tile-based enables efficient anti-aliasing
Cons
  Complex architecture
  High scene complexity can lower efficiency
  Need to add depth buffer for new standards
for each frame {
for each tile {
for each polygon {
render visible pixels
}
}
}
Geometry
Fragment
Renderer
Memory
Write Buffer
Read Texture
Primitives
Tiling
Color Buffer
Scene Data
Geometry
Primitives
Local Tile Buffer
Pre-rendering
Primitives Per Tile

## Slide 24: Mali Architecture: Hybrid Renderer
Pros
  Simpler hardware than fully deferred
  Lower bandwidth than immediate
  Scalable performance with resolution
  Tile-based enabled efficient anti-aliasing
Cons
  Geometry bandwidth
for each frame {
for each tile {
for each polygon {
render pixels
}
}
}
Geometry
Fragment
Renderer
Memory
Write Buffer
Read Texture
Primitives
Tiling
Color Buffer
Scene Data
Geometry
Primitives
Local Tile Buffer
Primitives Per Tile

## Slide 25: Mali Architecture: Mali Rendering Pipeline
Mali GPUs are Tile-Based Renderers (TBRs)
  Whole render targets (RTs) are rendered in a two-pass scheme
  First pass performs all vertex shading and assigns primitives to screen-space tiles
  Second pass performs all fragment shading, rendering one tile at a time
Rendering is deeply pipelined
  Vertex shading for RT N+1 runs at the same time as fragment shading for RT N
FS F2
VS+T F2
CPU F2
Time
FS F1
VS+T F1
CPU F1
FS F0
VS+T F0
CPU F0
Notes: Content with a single render target, which is hitting vsync often, lacks the right amount of rendering operations to maintain the pipeline, so the fragment shader for RT.N will finish before the vertex shader for RT.N+1 is actually available.
Content with multiple render targets per frame will often have vertex shading that is running ahead of the fragment shading by more than one render target. This is because the complexity of the targets is variable, and there are no strict data dependencies to force “in order” behavior.

## Slide 26: Mali Rendering Memory Traffic
Mali processes all geometry before processing fragment shading
  Geometry pass outputs are large, so must be written to main memory
          Vertex shader output: varyings
          Tiler output: polygon list
Mali processes each 16x16 pixel tile to completion
  Fragment shading working set is small, so can keep in local memory
          Blending and multi-sampling is inexpensive
          Tile written back to memory only when complete, allowing transaction elimination and compression
DDR
GPU
Vertex Shader
Vertex Attributes
Tiler
Geometry Working Set (Polygon List + Varyings)
Framebuffer
Textures
Local Tile Memory
Fragment Shader